VirtualHdos
HDOS Emulator
February 14, 2023

## Introduction
VirtualHdos is a JAVA program that emulates a HDOS OS running on a Z80 with 64K RAM. It is normally used to execute a single HDOS command, but is capable of handling “submit” files as well as native (on the host PC) text files filled with commands. Currently, it is only HDOS v2.0.

## Native Files
Native files must have lower-case only names. Mixed-case filenames will cause unpredictable results. All files created by HDOS programs will be in lower-case.

The file’s write permission is used to reflect the HDOS RO attribute. HDOS programs that change a file’s RO attribute will change the native file’s write permission.

The file’s execute permission is used to reflect the HDOS SYS attribute. Note that Windows will always show files as executable, and thus files on a Windows host will always have the SYS attribute set. Also remember that HDOS normally hides files that have the SYS attribute set. There is a server configuration setting that disables the SYS attribute, to avoid these issues on Windows hosts. Note that some non-Windows systems may set file execute bits incorrectly, such as ZIP archive extractions or files copied from a Windows system. On non-windows systems the execute permissions can be removed from HDOS files that should not be SYS.

Files that are not an even multiple of 256 bytes in size will be padded to a 256-byte multiple, using NUL (0x00), when reading. Writing to a file from HDOS always involves a full 256-byte record, so no additional padding is performed.

## Configuration
The emulator is configured using a “configuration file”, which is plan text formatted as “property = value” lines. The configuration file to be used is based on the following search order. First, it will look in the current directory for “vhdos.rc” and second in the user’s home directory for “.vhdosrc”. Comments in the file start with ‘#’ as the first non-space character of the line. Property values may use backslash (‘\’) to extend long values to the following line.

The following properties are recognized:

silent
Suppresses informative messages about configuration, etc.

vhdos_root_dir = path
Specifies the top-level (root) directory to be exported. Subdirectories named “sy0” through “sy3”, “dk0” .. “dk3”, are assumed, but not created automatically. Default will be ~/HostFileHdos. Note that JAVA Properties does not recognize the ‘~’ syntax, so the absolute path must be used.

vhdos_nosys
Disable the HDOS SYS attribute, so files will not be hidden on Windows.

vhdos_drive_X = path
Where “X” is one of “sy0” through “dk3”. Specify the path to use instead of “root_dir/X” for the HDOS drive.

vhdos_dump = file
Triggers a core dump of RAM when exiting the emulation. The dump file contains the raw (binary) contents of RAM. Note that subsequent dumps to the same file will overwrite any previous dump. Default file name is “vhdos.core”.

vhdos_trace = command
Enables program (instruction) tracing based on command. See section “Tracing”.

vhdos_cpu = cpu
Select which CPU to use. Value cpu may be “I8080”, “I8085”, “Z80”, or “Z180”. Default is Z80.

vhdos_disas = zilog
For Z80 and Z180 CPUs, this selects Zilog mnemonics in the disassembled instruction when tracing. Default is to use Intel mnemonics with standard macro syntax for Z80/Z180 instructions.
## Environment Variables
The following environment variables are recognized:

HDOSDrives = path-list
The path-list is a list of (up to) 8 paths separated by commas. Each path is positional dependent, i.e. the first path is for drive SY0:, second for drive SY1:, etc. If a path is empty (“,,”), then the default is used. All non-empty paths are translated into vhdos_drive_X properties.

HDOSDrive_X = path
Specifies the path to use for drive X. This is translated into a vhdos_drive_X properties.

VHDOSCoreDump = file
Triggers a core dump of RAM when exiting the emulation. The dump file contains the raw (binary) contents of RAM. Note that subsequent dumps to the same file will overwrite any previous dump. This overrides any vhdos_dump property. Default file name is “vhdos.core”.

VHDOSTrace = command
Enables program (instruction) tracing based on command. This overrides any vhdos_trace property in the config file. See section “Tracing”.

VHDOSCPU = cpu
Select which CPU to use. Value cpu may be “I8080”, “I8085”, “Z80”, or “Z180”. This overrides any vhdos_cpu property. Default is Z80.

VHDOSShow = drive
This variable causes vhdos to print the path being used for drive (“sy0”, ...) and exit without running any program or command. It may be used from Makefiles to directly access the HDOS files without using hard-coded paths.
## Running the Emulator
Typical startup command:

java -jar Virtualvhdos.jar hdos-command

Typically, a wrapper script or batch file will be created, to simplify running commands. On Linux, this might look like:

#!/bin/bash
exec java -jar /path/to/VirtualHdos.jar "${@}"

If this script were named “vhdos”, and is on the user’s PATH, then one would run HDOS commands using:

vhdos hdos-command

Note that this emulator does not provide any I/O hardware emulations. Any programs that execute input/output instructions will cause (non-fatal) messages to be printed for each I/O. While these are non-fatal incidents to the emulator, it is likely that the HDOS program will not run correctly.

On Linux/Unix systems (or compatible shells on Windows), a command may be prefixed by environment variables, which is a convenient way to do ad-hoc tracing and coredumps. For example:

VHDOSCoreDump=mydumpfile vhdos hdos-command

### Console Input
Translating HDOS console input to JAVA and modern “stdin” is problematic. This emulator is optimized for whole-line input, so some programs that use “raw” input may not work well. Programs doing full-line input should work fine, although because of echoing there is an extra blank line after entering input.

### Batch Execution (SUBMIT)
[NEEDS TESTING] Conventional HDOS 3 submit files may be executed as a command. In addition, a local (native) file may be used even though it does not reside on a HDOS drive. The file must be entered as a path, i.e. must contain a slash (‘/’), even if only a “./” prefix.

Each line is a command, or if prefixed with ‘<’ a line of input to the program being run at the time. Argument substitutions are supported, using the standard “$1”, “$2”, … “$9” notation. Comment lines must begin with ‘#’ or ‘;’. Empty lines are skipped.

There is no way to disable searching for “command.sub” when only “command” is entered, but entering “command.com” will avoid matching any submit file.
## Setup Example
Here is an example set of commands used on Linux to setup vhdos. These assume no vhdos config file is present. In this example, the repository ~/hdos-dist is used as a source for HDOS distribution files. Also, the ‘vhdos’ script has already been copied and edited and is on the user’s PATH.

$ mkdir -p ~/HostFileHdos/{sy0,sy1,sy2,sy3,dk0,dk1,dk2,dk3}
$ cp ~/hdos-dist/*.abs ~/HostFileHdos/sy0
$ vhdos hdos-command
...
$

The exact list of files, and order, above depends on what files were copied into the A: directory.

Note that any startup messages can be suppressed by setting up a vhdos config file that contains the “silent” property. For example, “echo silent >>vhdos.rc” in the current directory will add the ‘silent’ property, possibly creating a new “vhdos.rc” properties file.

## Makefile Example
Here is an example Makefile that uses vhdos to assemble using ASM.ABS into an ABS file, using source file “prog1.asm”. This makefile and the source file reside in the same directory. The default VirtualHdos SY0: drive must contain ASM.ABS and SY1: must contain any ACM files needed. Note that some of the vhdos commandline arguments may need to be quoted, because otherwise the host shell may try to interpret them or stumble over special characters.

export HDOSDrive_dk0 = $(PWD)

all: prog1.abs

%.abs: %.asm
        vhdos asm dk0:$*,dk0:$*=dk0:$*,sy1:/err

## Tracing
Trace commands take the form:

range [count] [oneshot]

Where range has the syntax:

low:high

A range expression of only ‘:’ matches the entire address range (a missing low or high equates to the respective end of the full address range). An expression of only low (no ‘:’) matches a single address. The high address is exclusive, i.e. a match means low <= PC < high.

A special range expression ‘.’ means immediate trigger, for use with specifying only count. This implies oneshot.

The count argument sets the number of instructions to be traced after matching the range. Note that this counter starts after “leaving” the range, i.e. all instructions within the range will always be traced. Default is 0 (no addition lines traced).

The oneshot keyword causes the tracing to occur only once. Tracing is essentially disabled after being triggered (after “leaving” the range).

The range argument is required and must be the first.